Auv project requirements
       1.Power Supply:
  1. Battery: Li-po 12V 2000mAh
  2. Voltage Regulators: LM 78XX series
2. Microcontroller or Processor:
  1. Arduino Mega 2650 / Raspberry Pi 3/4
  2. Servo motors-(optional) MG90S
3. Sensors:
  1. Depth Sensor: Negative z axis of the ypr from IMU Or MS5837-30BA
  2. IMU (Inertial Measurement Unit): Combine accelerometers, gyroscopes, and magnetometers to measure the AUV's orientation, acceleration, and angular velocity.
    MPU 9050
  3. Sonar:optional.
  4. GPS: INEO-6M GPS module for surface positioning and navigation.
  5. ph sensor -SEN 01XX
4. Communication:
  1. Wireless Communication: Use a communication module (e.g., Wi-Fi, Bluetooth, or RF) for remote control, data transfer, or telemetry.
  2. Ethernet: connectivity for onboard systems and data transfer.
5. Motor Control:
  1. Motor Drivers: L293D
  2. Thrusters: T200 with 7cm dia/ bilge pumps/ waterproofed BLDC motors with propellors
6. Data Storage and Logging:
  1. SD Card Module: Incorporate an SD card module to log sensor data and store mission-specific information.
7. Actuators:
  1. Additional Actuators: Depending on the AUV's design, include actuators such as servos or solenoids for specific tasks (e.g., payload deployment, sample collection, or camera movement).
  2. Camera : SV 16-HR
8. User Interface:
  1. LEDs/Displays:
  2. Buttons/Switches:

Specifications
- Determine the specific requirements and functionalities of the AUV's motherboard, such as the number and types of sensors, communication interfaces, power management, and motor control.
- Define the form factor and size constraints of the motherboard based on the AUV's physical design.
Schematic Design:
- Create a schematic diagram using Electronic Design Automation (EDA) software, such as Altium Designer or Eagle.
- Design the circuitry and connectivity for all components, including microcontrollers, sensors, communication modules, power regulators, and motor drivers.
- Ensure proper signal integrity, noise reduction, and adherence to design guidelines.
PCB Layout:
- Transfer the schematic design to the PCB layout software.
- Arrange and place the components on the PCB, considering factors like signal routing, power distribution, and thermal management.
- Route the traces to establish connections between components, considering signal integrity, noise minimization, and clearance constraints.
- Incorporate necessary ground and power planes for proper grounding and power distribution.
Prototype and Testing:
- Use the PCB layout files to create a prototype board.
- Order the PCB fabrication and assembly from a reliable manufacturer or assemble the board manually if feasible.
- Carefully solder the components onto the PCB.
- Perform thorough testing of the motherboard, including functional tests, signal integrity tests, and power consumption measurements.
Manufacturing and Production:
- Once the prototype board is successfully tested, you can proceed with manufacturing the final version of the motherboard in larger quantities.
- Submit the finalized PCB layout files to a reputable PCB manufacturer.
- Coordinate with the manufacturer to ensure the manufacturing process meets your specifications, including the choice of materials, surface finish, and solder mask.
Assembly and Integration:
- Assemble the manufactured PCBs with other components, such as connectors, headers, and mounting hardware.
- Ensure proper alignment, soldering, and secure mounting of all components.
- Connect the motherboard to other AUV subsystems, such as power distribution, communication systems, and motor control modules.
Testing and Debugging:
- Perform rigorous testing of the fully assembled motherboard to validate its functionality, performance, and reliability.
- Debug any issues or errors that may arise during testing and make necessary adjustments or modifications